Implementation of Routing in Plantage
Bachelor Thesis of Benedikt Schmidt
Supervisor: M.Sc. Pang-Yen Chou
Supervising Professor: PD Dr.-Ing. Helmut Gräb

---
Table of Contents
- analog circuits
- Plantage
- constraints for the layout
- claims
- overview of existing algorithms
- implemented algorithms
- results

---
Analog Circuits - Usage
surroundings are analog
used in communications engineering

---
Analog Circuits - Challenges
- exact voltage level
- problems with noise, temperature
- more complex layouts
- layout still often done manually

---
Plantage
- hierarchical placer
- several addition methods of shapes
- no routing (beside common centroids)
- produces several possible placements
  → shapefunction

---
Plantage

---
Plantage
- hierarchical placer
- several addition methods of shapes
- no routing (beside common centroids)
- produces several possible placements
  → shapefunction

---
Plantage

---
Constraints for the Layout
- not sensitive to noise
- not sensitive to temperature gradients
- not sensitive to process variation

---
Methods to fulfill the Constraints
- symmetries
- common centroids
- guard rings

---
Constraints for the Routing
- low resistance
- small capacitive couplings
- symmetric routes
- design rule clean

---
Design Rules
- minimum distance
- minimum enclosure
- minimum notch
- minimum width

---
Claims
- implementation of basic routing, considering
  - design rules
  - guard rings
  - symmetries
  - parasitics
- easy to replace by different algorithm

---
Overview of existing Algorithms
- basic algorithms
- steiner routing
- advanced algorithms
- template based router
- router integrated into the placer

---
Basic Algorithms
- Maze Router
- Line Router
- Channel Router

---
Steiner Routing

---
Advanced Algorithms
- mostly global-detailed algorithms
- examples:
  - ROSA
  - MIGHTY
  - ILAC
  - SALIM
  - SLAM
  - … and many more

---
Template Based Router
- requires an already routed layout
  - try to adapt to a different technology
- nearly full control by the designer

---
Router integrated into the Placer
- requires a placement algorithm with routing in mind
- routing wasn't included in the original idea of Plantage

---
Implemented Algorithms
- Line Expansion Router
  - no grid definition necessary
  - easy to implement
- modified version for pre-routing
- modified version for consideration of capacitive couplings

---
Line Expansion Router
- good directions
  - go as far as possible
- bad directions
  - go as far as necessary
- recursive
- chooses solution with smallest resistance
- terminates on maximum count of bends

---
Resistance
- only an estimation
- sheet resistance of the technology definition

---
Layers
- low priority layers
  - POLY1
- high priority layers
  - MET1
  - MET2
  - MET3
  - MET4

---
Select a Target
- done for every step, as a different target may be better now
- start area is selected similar

---
Good Directions
- straight towards the target
- along an obstacle
- for layer switch

---
Bad Directions
- beside an obstacle in front
- beside an obstacle behind
- for layer switch
- above (below) an obstacle

---
Layer Switch
- via is an obstacle on three layers
- minimum distance rules also on
  contacting-layers
- vias of current route may be also obstacles

---
Symmetric Routing
- connect symmetric pairs first
- connect rest to the net

---
Priorities of Possibilities
- differ on layer priority
- may stop if good enough result was found
Low
1. layer switch
2. enable layer switch
3. good directions
4. bad directions
High
1. good directions
2. layer switch
3. bad directions

---
Line Expansion Feasability Router
- only one result instead of several possibilities
- much faster than basic version
- useful as pre-router

---
Extended Line Expansion Router
- chooses connection with smallest objective
- objective is weighted sum of
  - resistance
  - edge capacitance
  - area capacitance
- reduces also capacitive parasitics

---
Area Capacitance
- capacity between two route parts on different layers
- area capacitance from technology definition

---
Edge Capacitance
- capacity between two route parts on the same layer
- edge capacitance from technology definition

---
Capacity Calculation
- horizontal and vertical route parts on every layer
- capacities between the parts on the same layer
- capacities between parts on different layers

---
Result – Line Expansion Router

---
Result – Extended Line Expansion Router

---
Result – Symmetry

---
Interactive Question-And-Answer

---
Simulation Results
MISSING

---
Results
- implementation of basic routing, considering
  - design rules
  - guard rings
  - resistance matching for symmetric routes
  - parasitics
- easy to replace by different algorithm

---
Results

---
Statistics - Plantage
	previous	after
lines of code	16018	44304
files	110	458
average lines of code per file	145	96
unit tests	0	1595
revisions in subversion	64	2037

---
Thank you for your attention.