Implementation of Routing in Plantage
Bachelor Thesis of Benedikt Schmidt
Supervisor: M.Sc. Pang-Yen Chou
Supervising Professor: PD Dr.-Ing. Helmut Gräb

---
Structure
- analog circuits
- Plantage
- constraints for the layout
- claims
- overview of existing algorithms
- implemented algorithm(s)
- results

---
Analog Circuits
surroundings are analog
used in for example communications engineering
- exact voltage level
- problems with noise, temperature
- more complex layouts
- layout still often done manually

---
Plantage
- hierarchical placer
- several addition methods of shapes
- no routing (beside common centroids)
- produces several possible placements → shapefunction

---
Constraints for the Layout
- not sensitive to noise
- not sensitive to temperature gradients

---
Methods to fulfill the Constraints
- symmetries
- common centroids
- guards

---
Constraints for the Routing
- low resistance
- small capacitive couplings
- symmetric routes
- design rule clean

---
Design Rules
- minimum distance
- minimum enclosure
- minimum notch
- minimum width

---
Claims
- Implementation of basic routing, considering
  - design rules
  - guard rings
  - symmetries
  - parasitics
- easy to replace by different algorithm

---
Overview of existing Algorithms
- basic algorithms
- steiner routing
- sophisticated algorithms
- template based router
- router integrated into the placer

---
Basic Algorithms
- Maze Router
- Line Router
- Channel Router

---
Steiner Routing

---
Sophisticated Algorithms
- most based on a global-detailed approach
- examples:
  - ROSA
  - MIGHTY
  - ILAC
  - SALIM
  - SLAM
  - … and many more

---
Template Based Router
- require an already routed layout
- try to adapt to for example another technology
- nearly full control by the designer

---
Router integrated into the Placer
- require an placement algorithm with routing in mind
- Plantage wasn't thought for this

---
Implemented Algorithm(s)
- Line Expansion Router
  - no grid definition necessary
  - easy to implement
- modified version for pre-routing
- modified version for consideration of capacitive couplings

---
Line Expansion Router
- good directions
  - go as far as possible
- bad directions
  - go as far as necessary
- recursive
- chooses solution with smallest resistance
- terminates on maximum count of bends

---
Resistance
- only estimation
- sheet resistance of the technology definition

---
Layers
- low priority layers
  - POLY1
- high priority layers
  - MET1
  - MET2
  - MET3
  - MET4

---
Select a Target
- Done for every step, as a different target may be better now
- Start area is selected similar

---
Good Directions
- straight towards the target
- beside an obstacle
- for layer switch

---
Bad Directions
- beside an obstacle in front
- beside an obstacle behind
- for layer switch
- above (below) an obstacle

---
Layer Switch
- via is obstacle on three layers
  - POLY1
  - CONT
  - MET1
- minimum distance rules also on contacting-layers
- vias of current route maybe also obstacles

---
Symmetries
- connect symmetric pairs first
- connect rest to the net

---
Priorities of Possibilities
- Differ on layer priority
- May stop if good enough result was found
Low
1. layer switch
2. enable layer switch
3. good directions
4. bad directions
High
1. good directions
2. layer switch
3. bad directions

---
Line Expansion Feasability Router
- only one result
- much faster than basic version
- useful as pre-router

---
Extended Line Expansion Router
- Chooses connection with smallest objective
- objective is weighted sum of
  - resistance
  - edge capacity
  - area capacity
- reduces also capacitive parasitics

---
Area Capacity
- capacity between two route parts on different layers
- area capacity from technology definition

---
Edge Capacity
- capacity between two route parts on same layer
- edge capacity from technology definition

---
Capacity Calculation
- Horizontal and vertical route parts on every layer
- Capacities between the parts on the same layer
- Capacities between parts on different layers

---
Result – Line Expansion Router

---
Result – Extended Line Expansion Router

---
Result – Symmetry

---
Interactive Question-And-Answer

---
Simulation Results
MISSING

---
Results
- Implementation of basic routing, considering
  - design rules
  - guard rings
  - symmetries
  - parasitics
- easy to replace by different algorithm

---
Statistics - Plantage
	previous	after
lines of code	16018	44304
files	110	458
average lines of code per file	145	96
unit tests	0	1595
revisions in subversion	64	2037

---
Thank you for your attention.